## Slide 1: Design, Development and Construction of a Magnetohydrodynamic Cocktail Stirrer
Carlos Gross Jones

## Slide 2: Problem
Density- and temperature-driven separation in cocktails

## Slide 3: Existing Solutions
Spoon, Swizzle Stick
Boring
Lab Stir Plate
Uses magnetic “pill”
  Possibility of cross-contamination
  Pill must be retrieved
Still pretty boring

## Slide 4: Proposal: Contactless Cocktail Stirrer
Truly contactless (no magnetic “pill”)
Uses magnetohydrodynamics
  Electrical and magnetic interactions with conductive fluid

## Slide 5: Magnetohydrodynamics
Well studied in marine propulsion
Simplest applications is Lorentz-force drive

## Slide 6: Early Efforts: 2013
Used direct insertion of current (electrodes in drink)
NdFeB permanent magnet
Advantages:
  Simple
  Provides good pumping
Disadvantages:
  Electrolysis of drink
  Electrically-driven erosion of electrodes

## Slide 7: Current effort: Magnetodynamic Coupling
Changing magnetic field induces currents (Faraday’s Law)
Eddy currents interact with original magnetic field (Lorentz force)
Commonly used in contactless braking systems

## Slide 8: Challenges
Root problem: cocktails are much less conductive than copper
  Requires large dB/dt to create significant force
  Increase field strength, rate of change, or both
Must meet budget and space constraints
  No superconductors, custom magnets, etc.
  Must fit in my living room

## Slide 9: Magnet Selection
Supermagnet from United Nuclear
3” dia., 1” thick
NdFeB 45

## Slide 10: Magnetostatic Analysis: FEMM
Used to characterize static field
Quadrupole arrangement provides stronger (maximum) field than dipole
1018 steel shunts to provide good return path
Maximum of 0.418 T in glass

## Slide 11: Magnetodynamic Analysis: Ansys Maxwell
Quadrupole assembly spun at 3600 RPM
Seawater used as conductivity baseline
Generates force vector field result
Maximum of 3.3 N/m3

## Slide 12: Computational Fluid Dynamics: OpenFOAM

## Slide 13: Conductivity Characterization
Experimental apparatus:
  ½” x ½” x 24” UHMW trough
  Capacitively-coupled plates at ends
  50 kHz sinusoidal excitation
Stages:
  Measure conductivity of precursors (liquor, mixers, etc.)
  Measure conductivity of common cocktails
  Optimize for conductivity

## Slide 14: Mechanical Design: Magnet Holders
Magnets contained in aluminum housings for mounting & protection
316 stainless steel (nonmagnetic) screws used

## Slide 15: Mechanical Design: Spinner Assembly
Assembly of four magnets into “spinner”
Steel shunts form part of spinner structure
Assembly anticipated to be challenging

## Slide 16: Mechanical Design: Frame
Speed (3600 RPM) and weight (~20 lb) of spinner assembly necessitate very robust structure
1.5” 80/20 extrusion frame

## Slide 17: Mechanical Design: Glass Support
Cocktail glass must be suspended in spinner assembly
Materials must be nonmagnetic and nonconductive
Delrin cup in Lexan ring

## Slide 18: Mechanical Design: Balancing
Spinner must be carefully balanced
Load cell on crossbar monitors centrifugal force
By correlating with shaft encoder, angular location of mass overburden can be found
Balance mass added on opposite side to balance spinner

## Slide 19: Mechanical Design: Power
12 VDC CIM motor drives spinner
Coupled to spinner shaft by #25 roller chain

## Slide 20: Control System
MDL-BDC24 PWM motor controller (40 A continuous)
  Internal PID loop for velocity control
  Controlled via CAN
National Instruments cRIO-9022 controller
  Realtime OS
  FPGA backplane
12 VDC, 50 A power supply

## Slide 21: Control System
cRIO monitors:
  Centrifugal force sensor
  Shaft encoder
  Motor voltage & current (via MDL-BDC24)
  User interface
And controls:
  MDL-BDC24
  Main power contactor

## Slide 22: Safety
cRIO shuts down motor if monitored parameters exceed safe limits
MDL-BDC24 can “brake” motor (short across armature)
“Emergency bushing” designed to limit maximum wobble of spinner
User behind barrier, at least for initial tests